## Slide 1
Soccer Wall
Wiring & Architecture Diagrams
April 2026 — Reference Document

## Slide 2
System Architecture — Control & Signal Path
User Device
Any phone/tablet/laptop
with a browser
ESP32
Web Server (192.168.4.1)
+ Modbus RTU Master
MAX485 Module
RS-485 Level Converter
WiFi
SOCCER_WALL / 192.168.4.1
UART2
RS-485 Bus
(Modbus RTU
57,600 baud)
SV660P Drive 1
Slave Address: 1
SV660P Drive 2
Slave Address: 2
Ethernet
CN4 → CN3
Motor 1 + Brake
MS1H4-40B30CB
Motor 2 + Brake
MS1H4-40B30CB
Linear Actuator 1
Left side of frame
Linear Actuator 2
Right side of frame
POWER SUPPLY OVERVIEW (wiring detail on slides 3 & 4)
24V Battery
TechCella
CAP-TC24100-NW
Y&H Inverter
RS-3200W
24V DC → 120V AC
Buck Converter
24V → 5V
for ESP32 logic
Brake Supply
24V wall wart
for motor brakes
Frame / Structure
~6×6 ft, ~90 lb

## Slide 3
AC Power Distribution — Inverter to Servo Drives
Y&H Inverter (RS-3200W)
BATTERY INPUT
AC OUTPUT
BATT+
BATT−
L
N
⏚
AC OUT
WAGO
WAGO
WAGO
SV660P Drive 1 (Slave Addr: 1)
SV660P Drive 2 (Slave Addr: 2)
AC INPUT
AC INPUT
L1
L2
PE
L1
L2
PE
Wire Colors:
Brown — L (Line)
Blue — N (Neutral)
Green/Yellow — PE (Protective Earth)
Wago lever connectors provide 3-way junction for each conductor (inverter + 2 drives).

## Slide 4
DC Power & Brake Wiring
A — Battery DC Input to Inverter
24V Battery
TechCella
CAP-TC24100-NW
BATTERY +
BATTERY −
(red circle / white plus)
(white circle / black minus)
Y&H Inverter (RS-3200W)
DC INPUT
DC +
DC −
24V +
24V −
Buck Converter
24V → 5V for ESP32 logic power
24V IN
5V OUT →
(tapped from 24V battery bus)
B — Brake Power Supply to Motor Brakes
Brake Power Supply
24V wall wart
(independent from inverter)
Brown
Blue
G/Y
stripped cable,
no connector
WAGO
WAGO
→ PE / chassis ground
Motor 1 — Brake Connector
Motor 2 — Brake Connector
BRAKE +
BRAKE −
BRAKE +
BRAKE −
(brown wire, ferrule)
(blue wire, ferrule)
(brown wire, ferrule)
(blue wire, ferrule)
Wire Colors:
Red — 24V DC+
Black — 24V DC−
Brown — Brake+ (no polarity on coil)
Blue — Brake− (no polarity on coil)
Green/Yellow — PE

## Slide 5
RS-485 Communications — Pin-Level Wiring Detail
ESP32
Microcontroller
MAX485 Module
RS-485 Level Converter
CN3
CN4
CN3
SV660P Drive 1
SV660P Drive 2
GPIO 17
(UART2 TX)
GPIO 16
(UART2 RX)
GPIO 4
(DE / RE)
GND
DI
RO
DE
RE
GND
A
B
GND
Pin 4 A
Pin 5 B
Pin 8 GND
Pin 4 A
Pin 5 B
Pin 8 GND
DE+RE
bridged
Assembled patch cable (RJ45 plug → CN3 socket)
CN3 and CN4 are internally
tied (pins physically shorted)
Straight-through
Ethernet cable
Wire Colors:
Green — UART2 TX (ESP32 → MAX485 DI)
Orange — UART2 RX / RS-485 A (RO out / A line)
Purple — DE/RE control / RS-485 B line
Black — Common GND
Blue — Ethernet daisy-chain (CN4 → CN3)
RJ45 pin numbering: 1–8 left-to-right looking at the connector face (tab down).
CN3 and CN4 are internally shorted on the SV660P — CN4 is a pass-through that daisy-chains the bus to the next drive.